## Slide 1: MobiWan NS-2 Simulation Platform to study mobility support in IPv6 Wide-Area Networks
Thierry Ernst
MOTOROLA Labs
and INRIA Rhône-Alpes
http://www.inrialpes.fr/planete/mobiwan

## Slide 2: Table of contents
Objective
Existing NS-2 Presentation
Missing Pieces in NS-2
New NS-2 Features for wide-area mobility and IPv6
  Topology Translation and Manipulation
  Inter-site Mobility
  Mobile IPv6
  Scenario Configuration
Conclusion

## Slide 3: Objective
Developing a simulation platform to study mobility support in Wide-Area IPv6 Networks
Necessary features:
  Playing with large topologies:
    Easy configuration and manipulation
  Local-area mobility (local mobility)
    mobility between adjacent cells of the same site
    geographical movement
    Access Routers are topologically close from one another
  Wide-area mobility (global mobility)
    mobility between sites and domains
    topological movement
    Access Routers are topologically distant from one another
  IPv6 capabilities
  Mobile IPv6 and Hierarchical Mobile IPv6
  Multicast capabilities at both wired and wireless nodes

## Slide 4: Objective: Mobility in a WAN
Local Mobiliy
(within a site)
Global Mobility
(between sites or domains

## Slide 5: Existing NS-2 Presentation
NS-2 (Network Simulator) from University of California at Berkeley
  Discrete time event simulator
  Object Oriented
  Developed under the VINT project
  Sponsored by Xerox Park, LBNL, USC/LSL
  http://www.isi.edu/nsnam/ns/index.html
Last release: NS-2.1b7 fall 2000
NS-2.1b8 currently under development
Code developed in C++ and OTcl (object TCL)

## Slide 6: Existing NS-2 Presentation: Features
Code: C++ and Otcl
Otcl - Object Tcl
  interpreted language
  does not require compilation
Each Class is mirrored both in C++ and OTCL
  Object variables may alternatively be accessed from C++ or OTCL
  Procedure calls between C++ and OTcl
OTCLmainly used:
    to aggregate objects to form various types of nodes
    to access objects from the interpreter
    to configure simulations
C++ mainly used
    to create base classes
    when more processing is required (routing table computation, mobility movement, …)

## Slide 7: Existing NS-2 Presentation: Features
Applications:
  CBR, HTML, TELNET, FTP, ...
Transport Protocols
  UDP, TCP, …
Routing Protocols
  Unicast (static / dynamic)
  Multicast (DVMRP, CBT)
Queue Models
Mobility
  Local Mobility within a geographical area
  Ad-Hoc routing protocols
  IEEE MAC 802.11
  Satellite constellations
  Mobile IPv4 (without routing optimization)

## Slide 8: Existing NS-2 Presentation: Using NS
Simulation configuration via a TCL script
  Create the network topology
  Simulation configuration
    Add protocols
    Create traffic
    Postpone events
  Run NS:
    Populate the neighborhood information for each node
    Static routing table is computed for each cluster
    Populate routing table for each node
    Schedule events
    Trace output
Results exploitation
    AWK - Perl - Gnuplot scripts

## Slide 9: Existing NS-2 Presentation: Nodes
Network topology = a collection of nodes and links
  Wired nodes (class Node) are connected by means of Links
  Wireless nodes (class MobileNode) are connected by means of Channels
Wired topologies:
  Class Node
    wired nodes only
    composed by a set of objects:
      Classifiers (static routing, port demux, etc)
      Agents ( i.e. objects simulating protocols [TCP, UDP, …])
  Class Link:
    composed by a set of objects:
      Queue Model
      TTL
      Trace

## Slide 10: Existing NS-2 Presentation: Mobile Nodes
Wireless topologies:
  Class MobileNode:
    wireless Nodes:
      Mobile Nodes
      Base Stations
        link Mobile Nodes to wired the wired topology
        = Mobile Nodes with speed=0
    composed by a set of objects inherited from Class Node
      + Ad-Hoc routing protocol
      + Link Layer
      + Queue
      + MAC
      + ARP
  Class Channel
    wireless broadcast medium (i.e. the air interface)
    propagation model
    delay = f(distance between sender/receiver + alpha)

## Slide 11: Existing NS-2 Presentation: Class MobileNode

## Slide 12: Existing NS-2 Presentation: Mobile IPv4

## Slide 13: Existing NS-2 Presentation: Local Mobility
Code contributed by CMU
Mobility within a limited geographical area
  Geographical area represented by a Grid
  Channel = wireless broadcast medium (i.e. the air interface) in the Grid
  Channel has a propagation model
    delay = f(distance between sender/receiver + alpha)
Mobility Model:
  Mobile Node is moving within the grid
  Mobile Node has a speed on moves towards a specified co-ordinate
  Explicit Movement:
    Specifies starting position and future destination
  Random Movement:
    chose randomly new position and speed

## Slide 14: Existing NS-2 Presentation: Local Mobility
Mobility within a geographical grid

## Slide 15: Existing NS-2 Presentation: Addressing
Hierarchical addresses:
3 layers:
  Domain
  Cluster
  Node
Hierarchy decreases routing table size
Each node has
  one entry per domain
  one entry per cluster in the same domain
  one entry per node in the same cluster

## Slide 16: Existing NS-2 Presentation: GT-ITM
Topologies may be generated using GT-ITM
  designed to model realistic Internet topologies
  produces graphs the reflect locality and hierarchy presents in the Internet
  uses the Transit-Stub model
  output is a graph in SGB format
Topics:
  arbitrary sizes ( from tens to thousands )
  2 kind of nodes:
    Transit Nodes ~ backbone nodes
    Stub Node ~ site routers

## Slide 17: Existing NS-2 Presentation: GT-ITM

## Slide 18: Existing NS-2 Presenation: from GT-ITM to NS
Translators sgb2ns - sgb2hierns
Input
  Graph in SGB format
Output:
  For each node, a NS OTCL call to create the node, and its address
    Addresses with 1 level of hierarchy for sgb2ns
    Addresses with 3 levels of hierarchy for sgbhierns
  Links between node numbers

## Slide 19: Existing NS-2 Presentation: GT-ITM
Parameters are:
  Type of model
  Number of transit domains
  Number of transit nodes / transit domain
  Number of stub domains / transit nodes
  Number of stub nodes per stub domain
  Probability for Transit nodes in same domain to be neighbors
  Probability for Stub nodes in same stub to be connected
  Stub domains may be connected (default is not)

## Slide 20: Missing Pieces in NS-2
Easy way to configure large topologies
Wide-area mobility
  Grid = limited geographical area
    how to expand a geographical area to the size of a WAN ?
    how to determine coordinates in a WAN ?
  Mobile Node cannot moves from one grid to another.
IPv6
Mobile IPv6
HMIPv6
Using MobileNode class and hierarchical addressing
Using Multicast and Wireless simultaneously

## Slide 21: Missing Pieces : Large Topologies Manipulation
Existing translator from GT-ITM to NS is not suitable to manipulate large topologies
  The function of the node in the topology is lost by the existing sgb2ns translator
We need to differentiate nodes according to their function in the topology:
  Transit Nodes are backbone routers
  Stub Nodes are routers within a site
  Nodes connecting stubs to a transit nodes are Border Routers
  Nodes connecting a wireless nodes to the wired network are Base Stations

## Slide 22: Missing Pieces: Large Topologies Manipulation

## Slide 23: New Features: Overview
Our enhancements are implemented in NS-2.1b6
2 main enhancements:
  1. Simulation Configuration for Large Topologies:
    TOPOGEN - topology generation
    TOPOMAN - topology manipulation
    SCEN TOOLS - simulation and topology configuration
    NS Addressing: 4 levels of hierarchy
  2. NS-2 Extensions for WAN mobility:
    Global Mobility: Mobility between sites
    Mobility management protocols: Mobile IPv6 / HMIPv6
    IPv6 Features
    Multicast Extensions for wireless nodes

## Slide 24: New Features: Overview

## Slide 25: New Features - 1: Simulation Configuration
Topology creation: TOPOGEN
    New translator from GT-ITM to NS format
    Output = TOPOMAN calls
Topology manipulation: TOPOMAN
    OTcl library to create, query and manipulate topologies of any size
Simulation scenario configuration: SCEN TOOLS
    Procedures to configure simulation scenario by querying TOPOMAN
Misc:
  IP addressing:
    NS hierarchical addressing ported from 3 levels to 4 levels
  Various TCL and shell scripts to configure simulations:
    HA, BS, CN selection
    mobility scenario

## Slide 26: New Features - 1: TOPOGEN Translator
Translator from GT-ITM to TOPOMAN calls
Input
  Graph in SGB format
Output:
  For each node, its id, site number, type
    Transit Router / Border Router / Site Router / Base Station
  We can also specify how many BSs we want in each site
    Translator computes their position within a grid according to grid size and # ( BS / site )
  Links between node numbers

## Slide 27: New Features - 1: TOPOMAN Library
A library of OTcl procedures to create, query, manipulate topologies of any size
  Before or after effective NS node creation
    Computation of routing table takes a while for large topologies
      we may want to display details about the topology before effectively running NS
    Node capabilities need to be specified before node creation
    Once effective NS node creation started, not possible to add new nodes

## Slide 28: New Features - 1: TOPOMAN Library
Input = TOPOMAN procedure calls (generated by TOPOGEN or by hand) that create:
  Administrative domains
  Sites
  nodes of specified type
Output:
  Array recording information for each node:
    Type of node (TN, BR, SR, BS, MN, more if needed)
    Node id
    Node IP address (according to its position in the topology)
  Misc Arrays to retrieve domain, site, etc, … the node belongs to

## Slide 29: New Features - 1: NS Addressing
Current NS addressing = 3 levels maximum
  Addressing need to be configured in a very precise way to avoid loops
    hard constraints
    no precise documentation available :-(
  3 levels:
    is not enough for large topologies
    still consume too much memory
We have ported NS addressing from 3 levels to 4 levels:
  A few HACKs in the OTCL scripts (mainly in ns-address.tcl)
    existing: domain_num_ + cluster_num + node_num
    we add: last_num_
    XXX: would be better to have something like level_[i]
  Modification in route.cc and route.h

## Slide 30: New Features - 1: NS Addressing

## Slide 31: New Features - 1: TOPOMAN Library
TOPOMAN alternatively produces NS addresses with:
    3 levels of hierarchy (NS binary compiled with the existing route.cc)
    4 levels of hierarchy (NS binary compiled with the enhanced route.cc)
With 4 levels of hierarchy:
    was technically impossible to give the same NS prefix to TNs in same domain:
      First level identifies the sub-domain within the topology
      A Domain comprise several sub-domain
      A Sub-domain always corresponds to a Transit Node
      First level = sub-domain => sub-domain prefix
      Second level = site within the sub-domain => site prefix
      Third level = subnet within site => subnet prefix
      Forth level = host within subnet
        Transit Nodes: <Sub-Domain prefix> .<Site id = 0>.<Subnet = 0>.0 e.g. 10.0.0.0
        BR / SR / BS: <Sub-Domain prefix>.<Site id # 0>.<Subnet id>.<0>: eg 10.1.0.0
        Mobile Nodes: <Sub-Domain prefix>.<Site id # 0>.<Subnet id>.<id # 0> eg:10.1.1.23

## Slide 32: New Features - 1: SCEN TOOLS Library
Library of procedures
  new features may be added at will
Uses TOPOMAN Library
Scenario specifies
  where do we want to attach Base Stations
  time at which site / base station is visited by the mobile node;
  which are the correspondent nodes;
  where are the Base Stations attached to;
  time at which correspondent nodes starts / stops;
Scenarios may be specified alternatively:
  in a file loaded in NS;
  by a procedure call in the simulation configuration script (preferred form)

## Slide 33: New Features - 1: SCEN TOOLS Library
Scenario procedures (e.g.):
  Visited Sites:
    select X sites in the topology
    every <interval> seconds, set Mobile Node to site Xi
  Correspondent Nodes:
    select X Site Routes in site 1
    enable Mobile IPv6 at each Xi and start traffic at time t
  Base Stations:
    select 3 Site Routers from each site
    attach 1 BS to each selected Site Router
  Mobile Node:
    select 1BS station in site 10 and uses it as the Home Agent
  Multicast
    select BR(s) for each site
    choose one of the BRs as the Rendez-Vous Point

## Slide 34: New Features - 1: Topology Manipulation
How to use TOPOMAN:
  Define your topology:
    global TOPOM
    if you want 3 levels of hierarchy (default) and you are using mobile node(s):
      set TOPOM [new Topoman ALL]
    if you are using topologies with wired nodes only :
      set TOPOM [new Topoman WIREDONLY]
    if you want to run very large topologies with mobile node(s) :
      set TOPOM [new Topoman ENHANCED]
      4 levels instead of 3 saves a lot of memory
      ( in order to use the ENHANCED mode, you also need to compile NS with an updated file route.cc - you can not use 4 levels and 3 levels with the same NS binary)
    load the topology with TOPOMAN calls (from file produced by TOPOGEN or by hand)

## Slide 35: New Features - 1: Topology Manipulation
  Configure your simulation:
      no need to effectively create nodes
      no need to call $ns_ run
    display the topology and various information
      Number of domains / sites / etc
    retrieve information about the topology
      queried by node_id / prefix / type of node / site id ...
      to retrieve all BRs, all Routers in site 10, ...
    Configure your simulation scenario:
      add 3 BSs in each site
      add a CN to each BR …
  Launch simulation:
    Call $TOPOM tm_create_topo which:
      configures NS addressing automatically (AddrParams)
      creates NS node objects
      add necessary capabilities depending on type of node
        e.g.: BS, CN and MN are running Mobile IPv6
      creates links
    $ns run

## Slide 36: New Features - 2: Extensions for WAN mobility
NS-2 Extensions for WAN mobility in IPv6:
  IPv6 Extensions
  Mobility management protocols:
    Mobile IPv6
    (Hierarchical Mobile IPv6 - coming soon)
  OTcl procedures
    to configure Class Node and Class Mobile Node
  Inter-site mobility (global mobility):
    Each site is associated with one channel
    Ability to move from site to site (i.e. from channel to channel)
  Misc extensions:
    multicast support for wirless nodes

## Slide 37: New Features - 2: IPv6
Just added necessary features in order for MIPv6 to work
IPv6 Extensions headers (simplified)
  Routing Header
Neighbour discovery (simplified)
  only between BSs and MNs
  Router Advertisements
  Router Solicitations
Routing Header processing at all nodes
Encapsulation / Decapsulation
  code contributed by SUN
  we just added:
    the Encapsulation object at all nodes
    Decapsulation at the mobile node
    (one line to change to add it at all nodes
Much more to add: any volunteer ?

## Slide 38: New Features - 2: Mobile IPv6
Implemented as a set of C++ / OTCL Agents
  Base Class = MIPv6
  Derived Classes: BS / HA / CN / MN
  Easy to add new derived classes (e.g.: HMIP MAP)
  OTCL configuration procedures
Features:
  Binding Updates and Binding Acknowledgements
  Route Optimization
  Automatic detection of CNs
  Routing Header from the CN
  Encapsulation from the HA
  Forwarding from the previous CoA to the new one
Missing Pieces
  Binding Requests management
  BU Piggybacking

## Slide 39: New Features - 2: MIPv6 for BS / HA and MN

## Slide 40: New Features - 2: MIPv6 for wired nodes (CN)

## Slide 41: New Features - 2: Inter-Site Mobility
Each site is associated with a “channel object”
  All sites have the same geographical size
  BSs in the same site listen and speak on the same channel
  BSs have (x,y) co-ordinates within the site boundaries
  MN may continue to move within the site using NS-2 existing Mobility Model developed by CMU
Moving from one site to another:
  MN changes the channel it is listening to
    netif_ points to the current channel
  does not require the MN to change its geographical coordinates
    The MN enters in a new site with the same coordinates it has in the previous site
    This does not interact with NS-2 existing mobility model:
      if a geographical movement is scheduled, it still will
Scenario determines time at which the Mobile Node may move from one site to another.

## Slide 42: New Features - 2: Inter-site mobility

## Slide 43: Conclusion
NS-2:
  Widely used
  Constantly evolving
Our NS-2 Enhancements:
  developed in the spirit of re-usability for other projects involving mobility support
  at time of start-up of this project, NS-2.1b3
  we did our best to follow NS-2 evolution
  our enhancements are working on NS-2.1b6
  NS team currently developing NS-2.1b8
  Hope that our code will be incorporated in the NS-2.1b8 distribution
  My wish is that developed features are going to be used by others
  Took a lot of time ; still much more to do
  many bugs and XXX in the code

## Slide 44: Thank you
Fore more information:
  Thierry Ernst
  http://www.inrialpes.fr/planete/mobiwan