## Slide 1: Extending Mobile IPv6 with Multicast to Support Mobile Networks in IPv6
Thierry Ernst - MOTOROLA Labs/ INRIA
Claude Castelluccia - INRIA Rhône-Alpes (project PLANETE)
Hong-Yon Lach - MOTOROLA Labs
http://www.inrialpes.fr/planete/people/ernst/Welcome.html

## Slide 2: Table of contents
Foreword:
  What are Mobile Networks and where do we find them ?
Aim
Review of the existing Mobile IPv6
Mobile Networks in Mobile IPv6:
  how to support mobile networks using Mobile IPv6 ?
  what are the problems ?
Extending Mobile IPv6 with Multicast
Conclusion

## Slide 3: Foreword: What is a mobile network ?
Mobile Network = Mobile Router + its attached Nodes and Routers
Distinct from Ad-hoc network: a network composed of mobile routers

## Slide 4: Foreword: What applications ?
Network of sensors deployed in aircrafts, boats, cars, trains, …
  traffic signaling data is exchanged with the Internet while every passenger is given access to the Internet (web surfing, remote connection to office, …)
Personal Area Networks (PANs)
  The network is made of all network elements carried by humans: cellular phone, notebook, …

## Slide 5: Mobile Networks: Aim of Mobility Support
To provide continuous Internet connectivity to nodes located in the mobile network
To offer optimal routing between Correspondent Nodes (CNs) and nodes in the mobile network (MNNs).
Notes: <number>
<footer>
<header>
July 30, 2026

## Slide 6: Review of Mobile IPv6
Working Group Mobile IP at the IETF.
Allow mobility of end-systems without communication disruption:
  mobile node MN is identified by its home address IP1 (address on the home link)
  a new temporary address IP2 (care-of address) is allocated to MN on each visited foreign link and is used for routing.
  MN is associated with a Home Agent HA (a router on the home link )
Notes: <number>
<footer>
<header>
July 30, 2026

## Slide 7: Review of Mobile IPv6: Mobiles nodes
First packets
  MN obtains care-of address IP2 from a router on the foreign link
  MN registers its current care-of address IP2 with its home agent HA.
  CN sends packets to the care-of address IP1
  HA intercepts, encapsulates, and redirects packets to care-of address IP2
  MN decapsulates packets
Following packets
  MN sends its care-of address to CN.
  CN sends packets directly to the care-of address IP2 using a IPv6 Routing Extension Header.
Notes: <number>
<footer>
<header>
July 30, 2026

## Slide 8
What does the Mobile IPv6 specification say ?
  Mobile IPv6 nodes may either be mobile hosts or mobile routers.
  But no explicit mention of mobile networks.
Could we support mobile networks as a Mobile Node ?
Review of Mobile IPv6: Mobiles networks
Notes: <number>
<footer>
<header>
July 30, 2026

## Slide 9: Mobile Networks with Mobile IPv6: Problems
What happens if we support mobile networks as any mobile node ?
  Router MNG is a mobile node
  Mobile router MNG has a home agent (HG)
  MNG obtains a care-of address on foreign link (DHCPv6)
  MNG sends Binding Updates to register its care-of address with its home agent HG and its CNs
  Home agent HG and CNs add an entry
  in their binding cache
=> No problem for the MNG to register
its careof address with HG and its CNs.
Notes: <number>
<footer>
<header>
July 30, 2026

## Slide 10: Mobile Networks with Mobile IPv6: Problems
What happens if CN sends a packet to MNG ?
  Packet is sent towards the initial point of attachment of MNG (i.e. HG)
  HG intercepts packet (proxy ARP)
  HG has an entry corresponding to the home address of MNG
  Packet is encapsulated to the MNG’s care-of address
=> No problem to send packets if
the mobile router MNG is the final
destination.
Notes: <number>
<footer>
<header>
July 30, 2026

## Slide 11: Mobile Networks with Mobile IPv6: Problems
What happens if CN sends a packet to MNN ?
  Packet is sent towards initial point of attachment of MNG (i.e. HG)
  HG intercepts packet (proxy ARP)
  HG does not have an entry corresponding to the destination address of MNN
  Packet is sent by HG to the default router (DR)
  DR resends the packet which is intercepted by HG and so on …
Home Agent HG is unable to
redirect packet if final destination
is not the mobile router MNG.
Communication between CNs
and MNNs is not possible via home network.
Notes: <number>
<footer>
<header>
July 30, 2026

## Slide 12: Mobile Networks with Mobile IPv6: Problems
What happens if we want direct routing between CNs and MNNs?
  How do CNs know how to route packets towards the FG ?
  CNs corresponding with MNNs do not receive Binding Updates sent by MNG
Direct communication between CNs and MNNs is not possible either.
Notes: <number>
<footer>
<header>
July 30, 2026

## Slide 13: Mobile Networks with Mobile IPv6: Problems
Routing perspective:
  distinction between nodes in the mobile network is only necessary for routing INSIDE the mobile network.
  from outside, the mobile network may virtually be perceived as a single mobile node with one address and `n` interfaces attached to it.
Could we enhance Mobile IPv6 so that CNs communicating with MNNs be also sent a Binding Update ?
  Who sends the Binding Update and how ?
  What care-of address is contained in the Binding Update ?
Notes: <number>
<footer>
<header>
July 30, 2026

## Slide 14: Mobile Networks with Mobile IPv6: Problems
Could the Binding Updates be sent by the MNG to CNs communicating with MNNs ?
  How does MNG keep track of CNs communicating with MNN ?
  MNG sends the care-of address to CNs on behalf of the MNNs.
    Security concerns
    The sender of BU is authenticated ; not the MNN ;
    care-of address of MNG won’t be used to reach MNN.
  BU can not be piggybacked on payload
  datagrams
Notes: <number>
<footer>
<header>
July 30, 2026

## Slide 15: Mobile Networks with Mobile IPv6: Problems
Could the Binding Updates be sent by MNNs to their CNs ?
  BUs are properly authenticated
  What care-of address ?
    Care-of address of MNG: How care-of address of MNG is distributed to MNNs ?
    Co-located care-of address: MNNs have to behave as Mobile Nodes.
  Mobility of network is not transparent to MNNs.
Notes: <number>
<footer>
<header>
July 30, 2026

## Slide 16: Mobile Networks with Mobile IPv6: Problems
In both cases:
  Changes are needed.
  One BU per {MNN,CN}
=> duplicate BUs at CNs communicating with
several MNNs
=> Explosion of Binding Updates if large number of CNs
Notes: <number>
<footer>
<header>
July 30, 2026

## Slide 17: Mobile Networks with Mobile IPv6: Constraints
Mobility transparency to nodes in the mobile network
  MNNs should not take part in mobility management
Scalability: Future needs require to consider (potentially large) mobile networks in IPv6
  a mobile network may contain hundreds of nodes
  each node of the mobile network may communicate with several CNs
    the mobile network may have thousands of CNs
    the number of CNs becomes a more important issue than the number of mobile networks.
  Optimal routing between CNs and the mobile network can not be left aside given the amount of expected traffic
  Minimum signaling is crucial given the number of potential BU recipients
Security and authentication of Binding Updates
  BU can not be sent on behalf of another node: BUs have to be sent by the node which obtains the care-of address.
Notes: <number>
<footer>
<header>
July 30, 2026

## Slide 18: Extending Mobile IPv6 with Network Scope BU
Problem:
  Communication between CNs and MNNs is not possible.
    How HG could redirect packets ?
    How to send a BU to MNNs’ correspondents ?
Observation:
  All nodes in the mobile network have the same network prefix
    (i.e a set of initial bits in the IPv6 address)
Solution:
  sending Binding Updates with a network scope
  instruct HA and CNs to route all packets bearing a network prefix corresponding to the prefix of the the mobile network via the MNG’s care-of address
  means:
    a new Sub-Option to carry network prefix
    recording a prefix in the binding cache: <network prefix, MNG care-of address>
    searching the binding cache for a prefix
  see draft-ernst-mobileip-v6-network-00.txt on the IETF’s web site
Notes: <number>
<footer>
<header>
July 30, 2026

## Slide 19: Extending Mobile IPv6 with Multicast
Problem:
  Binding Update explosion
    How to provide the care-of address of the MNG without overloading the network ?
Observation: all CNs receive the identical Binding Updates
Solution: sending BUs to the multicast group of CNs
  means:
    Each mobile network (i.e. MNG) is associated with a multicast address
    CNs are members of the multicast group / MNG is the only source
    Mobile Node is enhanced to Transmit BU using underlying IPv6 multicast
    A new resource record in the DNS to record the multicast address
Notes: <number>
<footer>
<header>
July 30, 2026

## Slide 20: Extending Mobile IPv6 with Multicast: How ?
Prior to first move:
  MNG gets a multicast address and registers it with DNS
Prior to communication set up:
  CN obtains IP address of MNN and multicast address from the DNS.
  CN joins multicast group.
At each subsequent move:
  MNG obtains a care-of address
  MNG sends BU containing its network prefix (home prefix) and its current care-of address to the multicast group.
Notes: <number>
<footer>
<header>
July 30, 2026

## Slide 21: Extending Mobile IPv6 with Multicast: How ?
CN receiving Binding Update:
  adds entry < network prefix ; MNG care-of address > in binding cache.
Sending packets to MNN:
  CN searches its binding cache for an entry corresponding to destination address
  prefix of destination address matches a prefix recorded in binding cache
  packet is sent to the MNN via MNG’s care-of address using a Routing Extension Header
  MNGs switches addresses and forward to MNN.
Notes: <number>
<footer>
<header>
July 30, 2026

## Slide 22: Extending Mobile IPv6 with Multicast: Evaluation
Advantages:
  No need to record addresses of CNs at the MNG (no binding list)
  One BU to update the location of the entire mobile network
  One entry per mobile network in binding cache
  BUs are authenticated (CNs are not misled)
  Mobility transparency to MNNs
  Optimal routing between CNs and MNNs
  Simple extensions to Mobile IPv6
Drawbacks:
  BU cannot be piggybacked
  No discrimination between recipients
  Cost of multicast signaling

## Slide 23: Conclusion
Mobile IPv6 does not support mobile networks at all
  We need to extend Mobile IPv6 with network scope Binding Updates
  Proposition made at 48th IETF 08/00.
Future needs require to consider (potentially large) mobile networks in IPv6.
  Due to the periodic emission of Binding Updates, Mobile IPv6 requires additional extensions to support large mobile networks efficiently.
  Multicast distribution of Binding Updates seems promising
  We are doing simulations to evaluate the use of multicast
Notes: <number>
<footer>
<header>
July 30, 2026

## Slide 24: Questions ?
For more information:
Thierry Ernst - MOTOROLA LABS / INRIA
Networking and Applications Lab (NAL)
Centre de Recherche de Motorola - Paris (CRM)
&
INRIA Rhône-Alpes - projet PLANETE
thierry.ernst@inrialpes.fr
http://www.inrialpes.fr/planete/people/ernst/Welcome.html