## Slide 1: Extending Mobile-IPv6 to Support Mobile Networks in IPv6
Thierry Ernst - MOTOROLA Labs/ INRIA
Claude Castelluccia - INRIA Rhône-Alpes (project PLANETE)
Hong-Yon Lach - MOTOROLA Labs
http://www.inrialpes.fr/planete/people/ernst/Welcome.html

## Slide 2: Table of contents
Foreword:
  What are Mobile Networks and where do we find them ?
Definitions and constraints
Review of the existing Mobile-IP
  Mobile Nodes in Mobile-IPv4
  Mobile Nodes in Mobile-IPv6
  Mobile Networks in Mobile-IPv4
Mobile Networks in Mobile-IPv6
  how to support mobile networks using Mobile-IPv6 ?
  what are the problems ?
Extending Mobile-IPv6 with Multicast
Conclusion

## Slide 3
Foreword: What is a Mobile Network ?
INTERNET

## Slide 4
Foreword: Applications of Mobile Networks
INTERNET
Network of sensors deployed in aircrafts, boats, cars, trains, …
  traffic signaling data is exchanged with the Internet while every passenger is given access to the Internet (web surfing, remote connection to office, …)
Personal Area Networks (PANs)
  The network is made of all network elements carried by humans: cellular phone, notebook, …

## Slide 5: Mobile Networks: Definitions
@ IP: identifies the location of the node in the Internet topology.
IP network: a set of nodes (i.e. hosts and routers) that share the same IP prefix and attached to the Internet through a single border router.
Network of mobiles: a network that contains mobile nodes.
Mobile Network: an IP network whose border router is dynamically changing its point of attachment to the Internet and thus its reachability in the IP topology.
Ad-hoc network: a network composed of mobile routers.

## Slide 6: Mobile Networks: Terminology
MN: Mobile Node.
CN: Correspondent Node.
MNN: Mobile Network Node Node inside the mobile network).
MNG: Mobile Network Gateway - border router of the mobile network which connects to the Internet.
HG: Home Gateway - initial point of attachment of the MNG.
FG(s): Foreign Gateway - subsequent points of attachment of the MNG.

## Slide 7: Mobile Networks: Assumptions
The mobile network has only one border router MNG.
The mobile network is a stub network, not a transit network.
The MNG is not multi-homed (it attaches to only one point of attachment HG or FG at a time).
HG and FGs are not themselves mobile.

## Slide 8: Mobile Networks: Characteristics
The internal architecture of the mobile network is preserved while roaming:
  nodes inside the mobile network do not move with respect to the MNG or with respect to one another
The MNG is a necessary transit router
Routing perspective:
  distinction between nodes in the mobile network is only necessary for routing INSIDE the mobile network.
  from outside, the mobile network may virtually be perceived as a single mobile node with one address and `n` interfaces attached to it.
Size of the mobile network:
  a mobile network may contain hundreds of nodes
  each node of the mobile network may communicate with several CNs
    the mobile network may have thousands of CNs
    the number of CNs becomes a more important issue than the number of mobile networks.

## Slide 9: Mobile Networks: Aim of Mobility Support
To provide continuous Internet connectivity to nodes located in the mobile network
To offer optimal routing between Correspondent Nodes (CNs) and nodes in the mobile network (MNNs).

## Slide 10: Mobile Networks: General Comments
Why shall we use IP ?
  IP is everywhere.
Why shall we use IPv6 and not IPv4 ? IPv6 features offer better support for:
  mobility
  security
  quality of service
  multicast,
  …
Problem ?
  Mobile-IP has not been designed to support specific characteristics of Mobile Networks.

## Slide 11: Review of the existing Mobile-IP
Working Group Mobile-IP at the IETF (Internet Engineering Task Force).
Allow mobility of end-systems without communication disruption:
  mobile node MN is identified by its home address IP1 (address on the home link)
  a new temporary address IP2 (careof address) is allocated to MN on each visited foreign link and is used for routing.
  MN is associated with a Home Agent HA (a router on the home link )

## Slide 12: Review of Mobile-IP: Mobile-IPv4 (RFC2002 and Internet Draft 2002-bis)
MN obtains careof address IP2 from FA on the foreign link
FA registers MN’s current careof address IP2 with MN’s HA
Correspondent Nodes (CNs) send packets to the home address IP1
HA encapsulates packets to the current careof address IP2.
FA decapsulates packets and forwards them to MN.
All packets from CN to MN transit through the HA while packets from MN to CN take the most direct path: Triangle Routing

## Slide 13: Review of Mobile-IP: Mobile-IPv4 with Routing Optimization (internet-draft)
Meanwhile, HA sends careof address to CNs of the MN.
CN sends packets directly to the careof address IP2 using tunneling
FA decapsulates packets and forwards them to MN.
MN obtains careof address IP2 from FA on the foreign link
FA registers MN’s current careof address IP2 with MN’s HA
CN sends packets to the home address IP1
HA intercepts, encapsulates, and redirects packets to careof address IP2.
FA decapsulates packets and forwards them to MN.
Following packets
First packets

## Slide 14: Review of Mobile-IP: Mobiles nodes with Mobile-IPv6
First packets
Following packets
MN sends its careof address to CN.
CN sends packets directly to the careof address IP2 using a IPv6 Routing Extension Header.
MN obtains careof address IP2 from a router on the foreign link
MN registers its current careof address IP2 with its home agent HA.
CN sends packets to the careof address IP1
HA intercepts, encapsulates, and redirects packets to careof address IP2
MN decapsulates packets

## Slide 15: Review of Mobile-IP: Mobile Networks in IPv4
Mobile-IPv4 (RFC2002) deals about Mobile Networks in section 4.5: “A mobile node can be a router responsible for the mobility of an entire network”.
mobile routers are supported as any other node
the point of attachment FG is a Foreign Agent.
mobile router MNG is allocated a new careof address from each subsequent foreign agent
foreign agent FG registers current careof address with mobile router’s Home Agent HG.
mobile router acts as a foreign agent for mobile nodes connected to the mobile network

## Slide 16: Review of Mobile-IP: Mobile Networks in IPv4
CN sends packets to the MNN
Packets are routed to the home link of the mobile network.
HG intercepts packets and encapsulates them to the home address of the mobile router and then to the careof address of the mobile router
FG decapsulates packets
Mobile router decapsulates packets again and forwards them to MNN
=> Mobile Networks are supported but routing is not optimal.

## Slide 17: Mobile Networks in Mobile-IPv6: What says the Mobile-IPv6 specification
In the Mobile-IPv6 specification, mobile nodes may either be a mobile host or a mobile router.
But no mention of mobile networks in the Mobile-IPv6 specification.

## Slide 18: Mobile Networks in Mobile-IPv6: Registration with home agent HG
What happens if we support mobile networks as in the Mobile-IPv4 specification ?
  mobile router MNG has a home agent (HG)
  MNG would obtain a careof address from the FG
  MNG would then register the careof address with its home agent HG.
  Home agent HG adds en entry in its binding cache

## Slide 19: Mobile Networks with Mobile-IPv6: First datagrams from the CN - triangle routing
CN sends packets to the initial point of attachment
HG intercepts and tunnels packets to the careof address of the MNG
MNG decapsulates and forwards.
=> packets transit by the home agent of the mobile network: non-optimal routing
How do CNs know how to route towards the mobile ?

## Slide 20: Mobile Networks with Mobile-IPv6: How could we optimize routing ?
How does MNG know CNs of MNNs ?
If Binding Update is sent on behalf of MNN, how is it authenticated by CNs ?
If Binding Update is not sent on behalf of MNNs, how does CNs understand that the careof address has to be used to communicate with MNN ?
Mobility of network is hidden to MNNs
Binding Updates can not be piggybacked on payload datagrams
What if Binding Updates are sent by MNG ?

## Slide 21: Mobile Networks with Mobile-IPv6: How could we optimize routing ?
How does MNN acquire the careof address ?
Which careof address should be used by MNN ?
  Careof address of MNG ?
  A distinct careof address for each MNN ?
MNN do take part in mobility management
  => Mobility of network is not transparent to MNNs
What if Binding Updates are sent by MNNs ?

## Slide 22: Mobile Networks in Mobile-IPv6: Problems
In both cases:
  Changes are required in the Mobile-IPv6 specification in order to support mobile networks.
  Authentification issues
  One BU per {MNN,CN}
    => duplicate BUs at CNs communicating with several MNNs
    => Binding Updates explosion if large number of CNs

## Slide 23: Mobile Networks in Mobile-IPv6: Constraints for a workable solution
Mobility transparency to nodes in the mobile network
  MNNs should not take part in mobility management
Scalability to large mobile networks
  Optimal routing between CNs and the mobile network can not be left aside given the amount of expected traffic
  Minimum signaling is crucial given the number of potential BU recipients
Security and authentication of Binding Updates
  BU can not be sent on behalf of another node: BUs have to be sent by the node which obtains the careof address.
Mobiles nodes visiting the mobile network
  make sure that MNN can keep using Mobile-IP

## Slide 24: Extending Mobile-IPv6 Using Multicast: Observation
All traffic transit through the MNG
All nodes in the mobile network have the same network prefix
  => tell CNs to route all packets bearing the network prefix of the MNG via its current FG
Inform CNs of the MNG’s careof address for all communications with a MNN
  => all CNs receive the same information
Why not using multicast then ?

## Slide 25
Extending Mobile-IPv6 Using Multicast: Proposed Enhancements
Proposed Enhancements:
Network scope binding updates:
  The Binding Update contains the network prefix of MNG
  Binding cache entries at CNs contains <network prefix, MNG careof address>
Multicast distribution of Binding Updates:
  Each mobile network (i.e. MNG) is associated with a multicast address
  CNs are members of the multicast group / MNG is the only source
  Transmit BU using underlying IPv6 multicast.
Necessary modifications:
Mobile-IPv6 modifications:
  a new IPv6 destination option to transmit the Network Binding Update
  addition of the MNG Operation (a enhanced Mobile Node Operation able to obtain a multicast address and to send BU to the multicast address
  The CN operation is enhanced to join the multicast group and understand the new IPv6 Destination Option:
A new resource record in the DNS to record the multicast address

## Slide 26: Extending Mobile-IPv6 Using Multicast: How it works
Prior to first move, MNG gets a multicast address and registers it with DNS
At each subsequent move, MNG obtains a careof address.
MNG sends BU containing its network prefix (home prefix) and its current careof address to the multicast group.
Meanwhile, CNs register to multicast group.
CNs receive BU and understand careof address of MNG should be used for all destinations bearing same network prefix as the MNG.
CNs send packets to the MNN via MNG careof address using a Routing Extension Header

## Slide 27: Mobile Networks with Mobile-IPv6: First datagrams from the CN - triangle routing

## Slide 28
Extending Mobile-IPv6 Using Multicast: Optimal Routing

## Slide 29
Extending Mobile-IPv6 Using Multicast: Evaluation
Advantages:
no need to record addresses of CNs at the MNG (binding list)
one BU to update the location of a mobile network
one entry per mobile network in binding cache
BUs are authenticated
Drawbacks:
BU cannot be piggybacked
No discrimination between recipients
Cost of multicast (for a small number of CNs)

## Slide 30: Conclusion
Future needs require to consider (potentially large) mobile networks in IPv6.
Mobile-IPv6 is not well adapted to support large mobile networks due to the periodic emission of Binding Updates
Mobile-IPv6 requires important modifications / extensions to support large mobile networks efficiently.
We need:
  to extend Mobile-IPv6
  or to propose new solutions
A solution based on multicast seems promising to support large mobile networks

## Slide 31: Questions ?
For more information:
Thierry Ernst - MOTOROLA LABS / INRIA
thierry.ernst@inrialpes.fr
at INRIA Rhône-Alpes - projet PLANETE
http://www.inrialpes.fr/planete/people/ernst/Welcome.html